## Slide 1: “Evolution and Performance” in [ Computer Organization and Assembly Language ] Lecture-02 M. M. Yasin myasin@ciitsahiwal.edu.pk

## Slide 2: [ Brief History of Computers ]
The First Generation:
  Vacuum Tubes…ENIAC (Electronic Numerical Integrator And Computer)
  (30 tones, 1500 sq ft, 18k vacuum tubes, consumes 140kw, capable of 5000 additions per sec…major drawback manual programming by setting switches and plugging/unplugging cables). Completed in 1946.
  VON Neumann Machine
    Idea of stored-program concept, referred to as the IAS (Princeton Institute for Advanced Studies).
    IAS computer is prototype of all subsequent general-purpose computers.

## Slide 3: [ Brief History of Computers ]
The First Generation:
  VON Neumann Machine
  …(got rid of manual programming and stored in memory alongside data… 1k storage locations of 40 binary digits).
    It has Mian Memory, ALU unit, Control unit, I/O equipment.
    40-bit Breakup: Each Word: 8-bit op-code, 12-bit address
    Registers: MBR, MAR, IR, IBR, PC, AC & MQ
    Completed after 1952.

## Slide 4: [ Brief History of Computers ]
The First Generation:
  …VON Neumann Machine
  21 instructions are grouped as follows:
    Data Transfer
    Unconditional Branch
    Conditional Branch
    Arithmetic
    Address Modify

## Slide 5: [ Brief History of Computers ]
The Second Generation:
  Transistors (invented in 1947 and launched in 1950s)
  (complex ALU & Control Unit, use of high level programming language)
The Third Generation:
  Integrated Circuits
  (got rid of discrete components of transistors, capacitors and resistors and their separate wiring on circuit board)

## Slide 6: [ Brief History of Computers ]
Later Generations:
  Large Scale Integration (or Integrated Circuit) (LSI)
  (More than 1000 components on single IC chip)
  Very Large Scale Integration (or Integrated Circuit) (VLSI)
  (More than 10,000 components on single IC chip)
  Ultra Large Scale Integration (or Integrated Circuit) (ULSI)
  (More than 1 million components on single IC chip)

## Slide 7
Generation | App. Dates | Technology | Speed (operation / sec)
1 | 1946-1957 | Vacuum Tube | 40, 000
2 | 1958-1964 | Transistor | 200, 000
3 | 1965-1971 | Small and Medium Scale integration | 1, 000, 000
4 | 1972-1977 | LSI | 10, 000, 000
5 | 1978-1991 | VLSI | 100, 000, 000
6 | 1991- | ULSI | 1, 000, 000, 000

## Slide 8: [ Brief History of Computers ]
Reducing Distance between Components
Decreasing Component Size
Increasing Memory Size
Increasing Processor Speed
Changing Organization of the Processor
“pipelining and parallel execution techniques”
“what’s the benefit of it????”
Balancing the performance of various elements