## Slide 1: “Introduction to Assembly Language Programming” Lecture-07 M. M. Yasin myasin@ciitsahiwal.edu.pk

## Slide 2
“Assembly Language and it’s Need”
Each family of Processors has its own set of instructions for handling various operations, called machine language instructions.
These are strings of 1s and 0s.
For a human-being to give instructions to computers or to develop software, it’s too complex to work on 1s and 0s.
So the low-level Assembly language is designed for a specific family of processors that represents various instructions in symbolic form for better understanding.

## Slide 3
“Advantages of Assembly Language”
Control the exact code behavior
Produce fast code; Less code memory and execution time
Powerful
Can produce hand-optimized code perfectly tuned for your particular hardware setup
Suitable for time-critical jobs like real-time processing
Provides knowledge of:
  How Program accesses I/O
  How instruction processes data
  Interface of programs with Operating System, Processors and BIOS
  (In short, it’s Fast, HW control and HW functional visibility)

## Slide 4
“Disadvantages of Assembly Language”
It is long and tedious to write
Errors can be very difficult to chase
Code can be fairly difficult to understand and modify.i.e., to Maintain and Debug
The result is non-portable to other Architectures, existing or upcoming
Your code will be optimized only for a certain implementation of a same architecture
Code must be heavily documented

## Slide 5
“High-Level versus Low-Level Language”
Instructions are much easier to remember and use than assembly language instructions.i.e., it’s more human-like.
High-level programs are much easier to understand than assembly language ones.
Fewer instructions are required to write a program than when using assembly language.
A program can usually be developed much more quickly using a high level language than an assembly language.
A program written in a high level language on one type of computer can usually be converted to operate on another type of computer quite easily.i.e., these are portable.

## Slide 6
“High-Level versus Low-Level Language”
High-level language programs normally take up more space and execute more slowly than equivalent assembly language programs.

## Slide 7
“Programming in Assembly Language”
Memory Segmentation:
Memory segments are a direct consequence of using a 20 bit address in a 16 bit processor
Memory is partitioned into 64K (216) segments
Each segment is identified by a 16-bit segment number ranging from 0000h-FFFFh
Within a segment, a memory location is specified by a 16-bit offset (the number of bytes from the beginning of the segment)
The Segment:Offset address is a logical address

## Slide 8
“Programming in Assembly Language”
Segment:Offset Addresses
A4FB:4872h means offset 4872h within segment A4FBh
To get the physical address, the segment number is multiplied by 16 (shifted 4 bits to the left) and the offset is added
A4FB0h + 4872h = A9822h (20 bit physical address)

## Slide 9
“Programming in Assembly Language”
8086 Registers
Information inside the microprocessor is stored in registers (fourteen 16-bit registers)
Data Registers hold data for an operation
Address Registers hold the address of an instruction or data
The Address Registers are divided into Segment, Pointer, and Index registers
A Status Register (called Flags) keeps the current status of the Processor

## Slide 10
“Programming in Assembly Language”
Data Registers: AX, BX, CX, & DX
Available to the programmer for general data manipulation
Some operations require a particular register
High and low bytes of data registers can be accessed separately, i.e., AX is divided into AH and AL
AX (Accumulator) is preferred for arithmetic, logic, and data transfer operations
BX (Base Register) serves as an Address Register
CX (Count Register) frequently serves as a loop counter
DX (Data Register) is used in multiplication and division

## Slide 11
“Programming in Assembly Language”
Pointer and Index Registers: SP, BP, SI, DI
SP (Stack Pointer) points to the top of the Processor's stack
BP (Base Pointer) usually accesses data (some place other than top) on the stack. Also used for indirect addressing similar to BX.
SI (Source Index) used to point to memory locations in the Data Segment
DI (Destination Index) performs same functions as SI.
Note: DI and SI are often used for string operations.

## Slide 12
“Programming in Assembly Language”
Segment Registers: CS, DS, SS, ES
CS (Code Segment) addresses the start of the program's machine code in memory
DS (Data Segment) addresses the start of the program's data in memory
SS (Stack Segment) addresses the start of the program's stack space in memory
ES (Extra Segment) addresses an additional data segment, if necessary

## Slide 13
“Programming in Assembly Language”
Instruction Pointer: IP
8086 uses registers CS and IP to access instructions
CS register contains the segment number of the next instruction and the IP contains the offset
The IP is updated each time an instruction is executed so it will point to the next instruction
Note: The IP is not directly accessible to the user

## Slide 14
“Programming in Assembly Language”
The FLAG Register
Indicates the status of the microprocessor
Two kinds of flag bits: Status Flags and Control Flags
Status flags reflect the result of an instruction, e.g., when the result of an arithmetic operation is 0, ZF (zero flag) is set to 1 (true)
Control flags enable or disable certain operations of the processor, e.g., if the IF (Interrupt Flag) is cleared (set to 0), inputs from the keyboard are ignored by the processor