## Slide 1: “The Computer Instruction Set” in [ Modern Computer Architecture ] Lecture-08 M. M. Yasin myasin@ciitsahiwal.edu.pk

## Slide 2
Instructions Groups and Concepts
Data Transfer Instructions
Arithmetic Instructions
Logic Instructions
Program/Flow Control Instructions
Processor/System Control Instructions
String Instructions
I/O Instructions

## Slide 3
Data Transfer Instructions
Register to Register
Register to Memory
Memory to Register
Memory to Memory
Arithmetic Instructions
ADD, SUB, MUL and DIV

## Slide 4
Logic Instructions
Boolean AND, OR, NOT and Exclusive- OR operations on a bit-by-bit basis.
These instructions also include shift instructions:
Arithmetic shift (left or right)
Logical shift (left or right)
Rotate shift (left or right) through or without carry flag

## Slide 5
Program/Flow Control Instructions
Unconditional Branch Instructions
Conditional Branch Instructions
Subroutine Call Instructions
Interrupt-handling Instructions

## Slide 6
Program/Flow Control Instructions
Subroutine Call Instructions
To carry out repeatedly needed tasks, saves space.
A large program is a collection of independent program modules, where each module may be a subroutine or a set of subroutines, this feature is called, in modern software approach, Modular Programming.
For example, in a multi-user system, several user programs may share the same I/O subroutine provided by the operating system.

## Slide 7
Program/Flow Control Instructions
Subroutine Call Instructions
Instructions used are:
CALL (refers to the first address of the subroutine) and
RET (usually the last instruction of the subroutine).
In microprocessors, PC is used as the Linkage Register to implement a subroutine call.

## Slide 8
Program/Flow Control Instructions
Interrupt-handling Instructions
It may be defined as a hardware-initiated subroutine call.
For example, in a microprocessor-based system, an I/O device such as a keyboard may generate an interrupt to inform the processor that valid data is available.

## Slide 9
Program/Flow Control Instructions
Interrupt-handling Instructions
When this interrupt is recognized, the processor suspends the execution of the currently running program,
Saves the contents of the PC in the stack, and
.
Transfers the control to a service routine dedicated to serve the keyboard.

## Slide 10
Program/Flow Control Instructions
Interrupt-handling Instructions
The service routine in this case reads the keyboard data, saves it in the main memory for further processing, and returns the control to the suspended program.
If the service routine needs the CPU registers, their previous contents must be saved in the stack before the service routine actually uses them.
Note: This is a time-consuming operations, to speed it up, some microprocessors uses duplicate registers to save time.

## Slide 11
Processor/System Control Instructions
Reset Instructions: Reset the processor, setting registers to initial values, clearing/setting interrupt, setting PC to a standard starting location, sending a reset signal to external devices. Halt instructions.
Halt Instructions: Brings the processor to an idle state until restarted by external action or interrupt.

## Slide 12
Processor/System Control Instructions
Now a days, systems are designed with multiprocessors to achieve high speed and more reliability.
In a typical multiprocessor environment, several processors share single memory. In this situation, at any given time only one processor should be allowed to access the shared memory. This problem is known as the Mutual Exclusion Problem.

## Slide 13
String Instructions
Each string instruction may require a source operand and destination operand or both.
SI and DI registers are used for source and destination respectively.
DS:SI and ES:DI pairs are used.
For example,
MOVS  Moves string data from memory to memory.
LODs  Load from memory
STOS  Saves to memory
CMPS  Compare two data items in memory
SCAS  Compares contents in register with memory

## Slide 14
I/O Instructions
To allow a processor to perform input and output operations.
An input instruction allows a peripheral to transfer a word to either a CPU register or memory.
Similarly an output instruction enables a processor to transfer a word into the buffer register of a peripheral device.
In some processors, peripheral device is mapped to a main memory address. In this situation, data moves from CPU to a memory location and vice versa constitute output and input operations. This method is known as Memory-mapped I/O.

## Slide 15
I/O Instructions
With Memory-mapped I/O approach, processor doesn't need any special I/O instruction.
Also, a programmer can exploit all the available addressing modes for performing I/O operations in an efficient manner.
A peripheral device can be mapped to an address in a separate address space called I/O space.
This would require special IN and OUT instructions.

## Slide 16
I/O Instructions
These are shorter than regular MOV instructions, and so program execution time is expedited.
Memory address space doesn't conflict with I/O space and entire memory can be completely utilized for storing code and data.

## Slide 17
I/O Instructions
Usually a processor is completely tied up with I/O operations. This limits the system's throughput (number of tasks processed per unit time) because the operational speed of a peripheral device is typically 20 to 50 times lower than the processor.
In order to overcome this difficulty, a hardware approach called Direct memory Access (DMA) is employed.

## Slide 18
I/O Instructions
In this method, the processor initiates an I/O operation by transferring typical parameters such as starting address in the memory, block size, and the type of operation, to a hardware device called a DMA controller. After this, the DMA controller takes control of the I/O transfer. The processor is free to do any computation after initializing the DMA controller.
Since I/O and CPU activities overlap, the DMA approach significantly increases a system's throughput.