## Slide 1: “The Computer Instruction Set” in [ Modern Computer Architecture ] Lecture-09 M. M. Yasin myasin@ciitsahiwal.edu.pk

## Slide 2
An Instruction manipulates the stored data.
Sequence of Instructions is called a Program.
Generally an instruction has two components:
  Op-code field
  Address field(s)
Op-code specifies how data is to be manipulated.
Address field indicates data address. It can be in the Processor and it can be in the Main Memory.

## Slide 3
[ Addressing Modes ]
Sequence of operations that a Processor carries out while executing an instruction is called instruction cycle (including determining addresses of the operands).
This determining of addresses, is called Addressing Mode.

## Slide 4
[ Addressing Modes ]
Inherent Addressing: If instruction’s Op-code indicates the address of the operand, which is usually the contents of the CPU Registers. For example,
MOV AX, BX ;( AXBX )
Whenever an instruction contains the operand value, it's called an Immediate Mode Instruction. For example,
Add AX, 25 ;( AX+25=AX )

## Slide 5
[ Addressing Modes ]
An instruction is said to have an Absolute Addressing Mode if it contains the address of the operand. For example,
MOV BX, [5000h] ;(BX  Contents of Memory location 5000)
Note: It can be used to write position-independent programs.

## Slide 6
[ Addressing Modes ]
A program is said to be Position-Independent , if it can be placed anywhere in the memory.
This is a desirable feature for operating system designers because…???

## Slide 7
[ Addressing Modes ]
An instruction is said to have a Register Mode if it contains a register address (as opposed to memory). In this case operand values are held in CPU registers. For example,
ADD CX, DX ;(CX  CX+DX)
Note: Large number of Registers are key characteristics of RISC based computers.

## Slide 8
[ Addressing Modes ]
Whenever an instruction specifies the address of a CPU register that holds the address of an operand, the resulting addressing mode is known as the Register Indirect Mode.
From this, it follows that the Effective Address(EA) of an operand in the Register Indirect Mode is the contents of the CPU register R, EA= (R). For example,
MOV [DX], [CX] ;[ DX  CX ]
CX = 500016 DX = 400016
[5000] 16 = 125616 [4000] 16 = 462916
i.e., CPU Register is used as a Data Pointer. What’s the Result?

## Slide 9
[ Addressing Modes ]
Two variations of the Register Indirect Mode are Auto-Increment and Auto-Decrement Modes.
In Auto-Increment,
first the contents of the specified CPU register are used as the address of the operand,
and then data transfer takes place,
then register contents are incremented automatically by some constant. For example,
MOV [DI]+, [SI] ;[DI]  [SI]

## Slide 10
[ Addressing Modes ]
Two variations of the Register Indirect Mode are Auto-Increment and Auto-Decrement Modes.
In Auto-Decrement,
first contents are decremented
then used as the address of the operand.
For example,
CLR –[CX]
Note: These modes are useful in array manipulation.

## Slide 11
[ Addressing Modes ]
Another important concept used in the context of addressing modes is Address Modification, that is,
EA (Effective Address) = RA (Ref. Address) + M (Modifier or Offset)
This address modification is used in:
Indexed Mode
Base-Register Mode
Relative Mode or Program Relative Mode

## Slide 12
[ Addressing Modes ]
In Indexed Mode, the value of RA is included in the instruction and a CPU register contains the value of M, usually called the Index Register...this could be used in accessing next array element.
While in Base Register Addressing Mode, RA is in separate register and M is included in the instruction, useful in virtual memory support.
In Program Relative Mode, Program Counter is used as RA and the contents of the second byte of the instruction is used as M.