## Slide 1: “8086 Instruction Set” Lecture-14 M. M. Yasin myasin@ciitsahiwal.edu.pk

## Slide 2
“Arithmetic Instructions”
ADD – ADD Destination, Source
ADC – ADC Destination, Source
These instructions add a number from some source to a number in some destination and put the result in the specified destination.
The ADC also adds the status of the carry flag to the result.
The source and destination cannot both be memory locations. If you want to add a byte to a word, you must copy the byte to a word location and fill the upper byte of the word with 0’s before adding.
Flags affected: AF, CF, OF, SF, ZF.

## Slide 3
“Arithmetic Instructions”
[ ADD Instruction Syntax ] Add <reg>,<reg> Add <reg>,<mem> Add <reg>,<const>
Add <mem>,<reg> Add <mem>,<const>
ADD AL, 74H ;Add immediate number 74H to content of AL
ADC CL, BL ;Add content of BL plus carry status to content of CL
ADD DX, BX ;Add content of BX to content of DX
ADD DX, [SI] ;Add word from memory at offset [SI] in DS to content of DX

## Slide 4
“Arithmetic Instructions”
SUB – SUB Destination, Source
SBB – SBB Destination, Source
These instructions subtract the number in some source from the number in some destination and put the result in the destination.
The SBB instruction also subtracts the content of carry flag from the destination.
The source and destination cannot both be memory locations. If you want to subtract a byte from a word, you must first move the byte to a word location such as a 16-bit register and fill the upper byte of the word with 0’s.
Flags affected: AF, CF, OF, PF, SF, ZF.

## Slide 5
“Arithmetic Instructions”
[ SUB Instruction Syntax ] Sub <reg>,<reg> Sub <reg>,<mem> Sub <reg>,<const>
Sub <mem>,<reg> Sub <mem>,<const>
SUB CX, BX ;CX – BX
SBB CH, AL ;Subtract content of AL and content of CF from content of CH
SUB AX, 3427H ;Subtract immediate number 3427H from AX
SBB BX, [3427H] ;Subtract word at displacement 3427H in DS and content of CF from BX

## Slide 6
“Arithmetic Instructions”
MUL – MUL Source
This instruction multiplies an unsigned byte in some source with an unsigned byte in AL register or an unsigned word in some source with an unsigned word in AX register.
When a byte is multiplied by the content of AL, the result (product) is put in AX. When a word is multiplied by the content of AX, the result is put in DX and AX registers.
MUL BH ;Multiply AL with BH; result in AX
MUL CX ;Multiply AX with CX; result high word in DX, low word in AX

## Slide 7
“Arithmetic Instructions”
MUL – MUL Source
MOV AX, MCAND_16 ;Load 16-bit multiplicand into AX
MOV CL, MPLIER_8 ;Load 8-bit multiplier into CL
MOV CH, 00H ;Set upper byte of CX to all 0’s
MUL CX ;AX times CX; 32-bit result in DX and AX

## Slide 8
“Arithmetic Instructions”
IMUL – IMUL Source
This instruction multiplies a signed byte from source with a signed byte in AL or a signed word from some source with a signed word in AX.
When a byte is multiplied by the content of AL, the result (product) is put in AX. When a word is multiplied by the content of AX, the result is put in DX and AX registers.
IMUL BH ;Multiply signed AL with signed BH; result in AX
IMUL AX ;Multiply AX with AX; result high word in DX, low word in AX
IMUL CX ;Multiply CX with AX; result high word in DX, low word in AX

## Slide 9
“Arithmetic Instructions”
DIV – DIV Source
This instruction is used to divide an unsigned word by a byte or to divide an unsigned double word (32 bits) by a word.
When a word is divided by a byte, the word must be in the AX register. The divisor can be in a register or a memory location. After the division, AL will contain the 8-bit quotient, and AH will contain the 8-bit remainder.
When a double word is divided by a word, the most significant word of the double word must be in DX, and the least significant word of the double word must be in AX. After the division, AX will contain the 16-bit quotient and DX will contain the 16-bit remainder.

## Slide 10
“Arithmetic Instructions”
DIV – DIV Source
If an attempt is made to divide by 0 or if the quotient is too large to fit in the destination (greater than FFH / FFFFH), the 8086 will generate a type 0 interrupt. All flags are undefined after a DIV instruction.
If you want to divide a byte by a byte, you must first put the dividend byte in AL and fill AH with all 0’s. Likewise, if you want to divide a word by another word, then put the dividend word in AX and fill DX with all 0’s.

## Slide 11
“Arithmetic Instructions”
DIV – DIV Source
DIV BL ;Divide word in AX by byte in BL; Quotient ;in AL, remainder in AH
DIV CX ;Divide down word in DX and AX by word in CX; Quotient in AX, and remainder in DX
DIV SCALE [BX] ;AX / (byte at effective address SCALE [BX]) if SCALE [BX] is of type byte;
or
(DX and AX) / (word at effective address SCALE[BX], if SCALE[BX] is of type word

## Slide 12
“Arithmetic Instructions”
IDIV – IDIV Source
This instruction is used to divide a signed word by a signed byte, or to divide a signed double word by a signed word.
When dividing a signed word by a signed byte, the word must be in the AX register. The divisor can be in an 8-bit register or a memory location. After the division, AL will contain the signed quotient, and AH will contain the signed remainder.
The sign of the remainder will be the same as the sign of the dividend.
If an attempt is made to divide by 0, the quotient is greater than 127 (7FH) or less than –127 (81H), the 8086 will automatically generate a type 0 interrupt.

## Slide 13
“Arithmetic Instructions”
IDIV – IDIV Source
When dividing a signed double word by a signed word, the most significant word of the dividend (numerator) must be in the DX register, and the least significant word of the dividend must be in the AX register. The divisor can be in any other 16-bit register or memory location. After the division, AX will contain a signed 16-bit quotient, and DX will contain a signed 16-bit remainder.
The sign of the remainder will be the same as the sign of the dividend.
Again, if an attempt is made to divide by 0, the quotient is greater than +32,767 (7FFFH) or less than –32,767 (8001H), the 8086 will automatically generate a type 0 interrupt.

## Slide 14
“Arithmetic Instructions”
IDIV – IDIV Source
IDIV BL ;Signed word in AX/signed byte in BL
IDIV BP ;Signed double word in DX and AX/signed word in BP
IDIV BYTE PTR [BX] ;AX / byte at offset [BX] in DS

## Slide 15
“Arithmetic Instructions”
INC – INC Destination
The INC instruction adds 1 to a specified register or to a memory location.
AF, OF, PF, SF, and ZF are updated, but CF is not affected.
This means that if an 8-bit destination containing FFH or a 16-bit destination containing FFFFH is incremented, the result will be all 0’s with no carry.

## Slide 16
“Arithmetic Instructions”
INC – INC Destination
INC BL ;Add 1 to contents of BL register
INC CX ;Add 1 to contents of CX register
INC BYTE PTR [BX] ;Increment byte in data segment at offset contained in BX
INC WORD PTR [BX] ;Increment the word at offset of [BX] and [BX+1] in the data segment
INC TEMP ;Increment byte or word named TEMP in the data segment
INC PRICES [BX] ;Increment element pointed to by [BX] in array PRICES

## Slide 17
“Arithmetic Instructions”
DEC – DEC Destination
This instruction subtracts 1 from the destination word or byte. The destination can be a register or a memory location.
AF, OF, SF, PF, and ZF are updated, but CF is not affected. This means that if an 8-bit destination containing 00H or a 16-bit destination containing 0000H is decremented, the result will be FFH or FFFFH with no carry (borrow).

## Slide 18
“Arithmetic Instructions”
DEC – DEC Destination
DEC CL ;Subtract 1 from content of CL register
DEC BP ;Subtract 1 from content of BP register
DEC BYTE PTR [BX] ;Subtract 1 from byte at offset [BX] in DS
DEC WORD PTR [BP] ;Subtract 1 from a word at offset [BP] in SS
DEC COUNT ;Subtract 1 from byte or word named COUNT in DS

## Slide 19
“Arithmetic Instructions”
CBW (CONVERT SIGNED BYTE TO SIGNED WORD)
This instruction copies the sign bit of the byte in AL to all the bits in AH. AH is then said to be the sign extension of AL. CBW does not affect any flag.
Suppose, AX = 00000000 10011011 (–155 decimal)
CBW ;Convert signed byte in AL to signed word in AX
Result is, AX = 11111111 10011011 (–155 decimal)

## Slide 20
“Arithmetic Instructions”
CWD (CONVERT SIGNED WORD TO SIGNED DOUBLE WORD)
This instruction copies the sign bit of a word in AX to all the bits of the DX register. In other words, it extends the sign of AX into all of DX. CWD affects no flags.
Suppose, DX = 00000000 00000000, and
AX = 11110000 11000111 (–3897 decimal)
CWD ; Convert signed word in AX to signed double word in DX:AX
Result is, DX = 11111111 11111111
AX = 11110000 11000111 (–3897 decimal)