## Slide 1: “8086 Instruction Set” Lecture-16 M. M. Yasin myasin@ciitsahiwal.edu.pk

## Slide 2
“Logical Instructions”
AND – AND Destination, Source
This instruction ANDs each bit in a source byte or word with the same numbered bit in a destination byte or word. The result is put in the specified destination. The content of the specified source is not changed.
The source can be an immediate number, the content of a register, or the content of a memory location.
The destination can be a register or a memory location.
The source and the destination cannot both be memory locations.

## Slide 3
“Logical Instructions”
AND – AND Destination, Source
CF and OF are both 0 after AND.
PF, SF, and ZF are updated by the AND instruction.
AND CX, [SI] ;AND word in DS at offset [SI] with word in CX register; Result in CX register
AND BH, CL ;AND byte in CL with byte in BH; Result in BH
AND BX, 00FFH ;00FFH Masks upper byte, leaves lower byte unchanged.

## Slide 4
“Logical Instructions”
OR – OR Destination, Source
This instruction ORs each bit in a source byte or word with the same numbered bit in a destination byte or word. The result is put in the specified destination. The content of the specified source is not changed.
The source can be an immediate number, the content of a register, or the content of a memory location.
The destination can be a register or a memory location.
The source and the destination cannot both be memory locations.

## Slide 5
“Logical Instructions”
OR – OR Destination, Source
CF and OF are both 0 after OR.
PF, SF, and ZF are updated by the OR instruction.
OR AH, CL ;CL ORed with AH, result in AH
OR BP, SI ;SI ORed with BP, result in BP
OR SI, BP ;BP ORed with SI, result in SI
OR BL, 80H ;BL ORed with immediate number 80H
OR CX, TABLE [SI] ;CX ORed with word from effective address TABLE[SI]

## Slide 6
“Logical Instructions”
XOR – XOR Destination, Source
This instruction Exclusive-ORs each bit in a source byte or word with the same numbered bit in a destination byte or word. The result is put in the specified destination. The content of the specified source is not changed.
The source can be an immediate number, the content of a register, or the content of a memory location.
The destination can be a register or a memory location.
The source and the destination cannot both be memory locations.

## Slide 7
“Logical Instructions”
XOR – XOR Destination, Source
CF and OF are both 0 after XOR.
PF, SF, and ZF are updated by the XOR instruction.
XOR CL, BH ;Byte in BH exclusive-ORed with byte in CL XOR BP, DI ;Word in DI exclusive-ORed with word in BP
XOR WORD PTR [BX], 00FFH
;Exclusive-OR immediate number 00FFH with word at offset [BX] in the data segment.

## Slide 8
“Logical Instructions”
NOT – NOT Destination
The NOT instruction inverts each bit (forms the 1’s complement) of a byte or word in the specified destination.
The destination can be a register or a memory location.
This instruction does not affect any flag.
NOT BX ;Complement content or BX register
NOT BYTE PTR [BX] ;Complement memory byte at offset [BX] in data segment.

## Slide 9
“Logical Instructions”
NEG – NEG Destination
This instruction replaces the number in a destination with its 2’s complement (inverts each bit and add one).
The destination can be a register or a memory location.
The NEG instruction updates AF, AF, PF, ZF, and OF.
NEG AL ;Replace number in AL with its 2’s complement
NEG BX ;Replace number in BX with its 2’s complement
NEG BYTE PTR [BX] ;Replace byte at offset BX in DS with its 2’s complement
NEG WORD PTR [BP] ;Replace word at offset BP in SS with its 2’s complement

## Slide 10
“Logical Instructions”
CMP – CMP Destination, Source
This instruction compares a byte/word in the specified source with a byte/word in the specified destination.
The source can be an immediate number, a register, or a memory location.
The destination can be a register or a memory location. However, the source and the destination cannot both be memory locations.
The comparison is actually done by subtracting the source byte or word from the destination byte or word. The source and the destination are not changed, but the flags are set to indicate the results of the comparison.

## Slide 11
“Logical Instructions”
CMP – CMP Destination, Source
AF, OF, SF, ZF, PF, and CF are updated by the CMP instruction.
For the instruction CMP CX, BX , the values of CF, ZF, and SF will be as follows:
 | CF | ZF | SF | 
CX = BX | 0 | 1 | 0 | Result of subtraction is 0
CX > BX | 0 | 0 | 0 | No borrow required, so CF = 0
CX < BX | 1 | 0 | 1 | Subtraction requires borrow, so CF = 1

## Slide 12
“Logical Instructions”
CMP – CMP Destination, Source
CMP AL, 01H ;Compare immediate number 01H with byte in AL
CMP BH, CL ;Compare byte in CL with byte in BH
CMP CX, TEMP ;Compare word in DS at displacement TEMP with word at CX
CMP PRICES [BX], 49H ;Compare immediate number 49H with byte at offset [BX] in array PRICES

## Slide 13
“Logical Instructions”
TEST – TEST Destination, Source
This instruction ANDs the byte / word in the specified source with the byte / word in the specified destination. Flags are updated, but neither operand is changed.
The test instruction is often used to set flags before a Conditional jump instruction.
The source can be an immediate number, the content of a register, or the content of a memory location. The destination can be a register or a memory location.
The source and the destination cannot both be memory locations.
CF and OF are both 0’s after TEST. PF, SF and ZF will be updated to show the results of the destination.

## Slide 14
“Logical Instructions”
TEST – TEST Destination, Source
TEST AL, BH ;AND BH with AL. No result stored; Update PF, SF, ZF
TEST CX, 0001H ;AND CX with immediate number 0001H; No result stored; Update PF, SF, ZF
TEST BP, [BX][DI] ;AND word at offset [BX][DI] in DS with word in BP. No result stored. Update PF, SF, and ZF