## Slide 1: “8086 Instruction Set” Lecture-17 M. M. Yasin myasin@ciitsahiwal.edu.pk

## Slide 2
“Logical Instructions”
RCL – RCL Destination, Count
This instruction rotates all the bits in a specified word/byte some number of bit positions to the left. The operation is circular because the MSB of the operand is rotated into the carry flag and the bit in the carry flag is rotated around into LSB of the operand.
The destination can be a register or a memory location.
To rotate by more than one bit position, load the desired number into the CL register and put “CL” in the count position of the instruction.

## Slide 3
“Logical Instructions”
RCL – RCL Destination, Count
RCL DX, 1 ;Word in DX 1 bit left, MSB to CF, CF to LSB
MOV CL, 4 ;Load the number of bit positions to rotate into CL
RCL SUM [BX], CL ;Rotate byte or word at effective address SUM [BX] 4 bits left Original bit 4 now in CF, original CF now in bit 3.
MSB
CF
LSB

## Slide 4
“Logical Instructions”
RCR – RCR Destination, Count
This instruction rotates all the bits in a specified word or byte some number of bit positions to the right. The operation circular because the LSB of the operand is rotated into the carry flag and the bit in the carry flag is rotate around into MSB of the operand.
The destination can be a register or a memory location.
To rotate by more than one bit position, load the desired number into the CL register and put “CL” in the count position of the instruction.

## Slide 5
“Logical Instructions”
RCR – RCR Destination, Count
RCR BX, 1 ;Word in BX right 1 bit, CF to MSB, LSB to CF
MOV CL, 4 ;Load CL for rotating 4 bit position
RCR BYTE PTR [BX], 4 ;Rotate the byte at offset [BX] in DS 4 bit positions right CF = original bit 3, Bit 4 – original CF
MSB
CF
LSB

## Slide 6
“Logical Instructions”
ROL – ROL Destination, Count
This instruction rotates all the bits in a specified word or byte to the left some number of bit positions. The data bit rotated out of MSB is circled back into the LSB. It is also copied into CF. In the case of multiple-bit rotate, CF will contain a copy of the bit most recently moved out of the MSB.
The destination can be a register or a memory location.
To rotate by more than one bit position, load the desired number into the CL register and put “CL” in the count position of the instruction.

## Slide 7
“Logical Instructions”
ROL – ROL Destination, Count
ROL AX, 1 ;Rotate the word in AX 1 bit position left, MSB to LSB and CF
MOV CL, 04H ;Load number of bits to rotate in CL
ROL BL, CL ;Rotate BL 4 bit positions
ROL FACTOR [BX], 1 ;Rotate the word or byte in DS at EA = FACTOR [BX] by 1 bit position left into CF
MSB
CF
LSB

## Slide 8
“Logical Instructions”
ROR – ROR Destination, Count
This instruction rotates all the bits in a specified word or byte some number of bit positions to right. The bit moved out of the LSB is rotated around into the MSB. The data bit moved out of the LSB is also copied into CF. In the case of multiple bit rotates, CF will contain a copy of the bit most recently moved out of the LSB.
The destination can be a register or a memory location.
To rotate by more than one bit position, load the desired number into the CL register and put “CL” in the count position of the instruction.

## Slide 9
“Logical Instructions”
ROR – ROR Destination, Count
ROR BL, 1 ;Rotate all bits in BL right 1 bit position LSB to MSB and to CF
MOV CL, 08H ;Load CL with number of bit positions to be rotated
ROR WORD PTR [BX], CL ;Rotate word in DS at offset [BX] 8 bit position right
MSB
CF
LSB