## Slide 1: “8086 Instruction Set” Lecture-19 M. M. Yasin myasin@ciitsahiwal.edu.pk

## Slide 2
“String Manipulation Instructions”
MOVS – MOVS Dest. String Name, Source String Name
MOVSB – MOVSB Dest. String Name, Source String Name
MOVSW – MOVSW Dest. String Name, Source String Name
This instruction copies a byte or a word from location in the data segment to a location in the extra segment.
The offset of the source in the data segment must be in the SI register.
The offset of the destination in the extra segment must be in the DI register.
For multiple-byte or multiple-word moves, the number of elements to be moved is put in the CX register so that it can function as a counter.

## Slide 3
“String Manipulation Instructions”
MOVS – MOVS Dest. String Name, Source String Name
MOVSB – MOVSB Dest. String Name, Source String Name
MOVSW – MOVSW Dest. String Name, Source String Name
After the byte or a word is moved, SI and DI are automatically adjusted to point to the next source element and the next destination element.
If DF is 0, then SI and DI will incremented by 1 after a byte move and by 2 after a word move.
If DF is 1, then SI and DI will be decremented by 1 after a byte move and by 2 after a word move.

## Slide 4
“String Manipulation Instructions”
MOVS – MOVS Dest. String Name, Source String Name
MOVSB – MOVSB Dest. String Name, Source String Name
MOVSW – MOVSW Dest. String Name, Source String Name
In MOVS, The assembler will code the instruction for a byte / word move if they were declared with a DB / DW. MOVSB says move a string as bytes; MOVSW says move a string as words.
MOV SI, OFFSET SOURCE ;Load offset of start of source string in DS into SI
MOV DI, OFFSET DEST ;Load offset of start of destination string in ES into DI
CLD ;Clear DF to auto increment SI and DI after move
MOV CX, 04H ;Load length of string into CX as counter
REP MOVSB ;Move string byte until CX = 0

## Slide 5
“String Manipulation Instructions”
LODS / LODSB / LODSW
(LOAD STRING BYTE INTO AL OR STRING WORD INTO AX)
This instruction copies a byte from a string location pointed to by SI to AL, or a word from a string location pointed to by SI to AX.
If DF is 0, SI will be automatically incremented (by 1 for a byte string, and 2 for a word string) to point to the next element of the string.
If DF is 1, SI will be automatically decremented (by 1 for a byte string, and 2 for a word string) to point to the previous element of the string.

## Slide 6
“String Manipulation Instructions”
LODS / LODSB / LODSW
(LOAD STRING BYTE INTO AL OR STRING WORD INTO AX)
CLD ;Clear direction flag so that SI is auto-incremented
MOV SI, OFFSET SOURCE ;Point SI to start of string
LODS ;Copy a byte/word from string to AL/AX
Note:
The assembler uses the name of the string to determine whether the string is of type bye or type word. Instead of using the string name to do this, you can use the mnemonic LODSB to tell the assembler that the string is of type byte or LODSW to tell the assembler that the string is of type word.

## Slide 7
“String Manipulation Instructions”
STOS / STOSB / STOSW
(STORE STRING BYTE OR STRING WORD)
This instruction copies a byte from AL or a word from AX to a memory location in the extra segment pointed to by DI.
Same previous rule for Direction Flag (DF) applies.
MOV DI, OFFSET TARGET
STOS

## Slide 8
“String Manipulation Instructions”
CMPS / CMPSB / CMPSW
(COMPARE STRING BYTES OR STRING WORDS)
This instruction can be used to compare a byte / word in one string with a byte / word in another string.
SI is used to hold the offset of the byte or word in the source string, and DI is used to hold the offset of the byte or word in the destination string. Same previous rule for Direction Flag (DF) applies.
The AF, CF, OF, PF, SF, and ZF flags are affected by the comparison, but the two operands are not affected.

## Slide 9
“String Manipulation Instructions”
CMPS / CMPSB / CMPSW
(COMPARE STRING BYTES OR STRING WORDS)
The CMPS instruction can be used with a REPE or REPNE prefix to compare all the elements of a string.
MOV SI, OFFSET FST ;Point SI to source string
MOV DI, OFFSET SEC ;Point DI to destination string
CLD DF ;cleared, SI and DI will auto-increment after compare
MOV CX, 100 ;Put number of string elements in CX
REPE CMPSB ;Repeat the comparison of string bytes until end of string or until compared bytes are not equal

## Slide 10
“String Manipulation Instructions”
SCAS / SCASB / SCASW
(SCAN A STRING BYTE OR A STRING WORD)
SCAS compares a byte in AL or a word in AX with a byte or a word in ES pointed to by DI. Therefore, the string to be scanned must be in the extra segment, and DI must contain the offset of the byte or the word to be compared.
SCAS affects AF, CF, OF, PF, SF, and ZF, but it does not change either the operand in AL (AX) or the operand in the string.

## Slide 11
“String Manipulation Instructions”
SCAS / SCASB / SCASW
(SCAN A STRING BYTE OR A STRING WORD)
The following program segment scans a text string of 80 characters for a carriage return, 0DH, and puts the offset of string into DI:
MOV DI, OFFSET STRING
MOV AL, 0DH ;Byte to be scanned for into AL
MOV CX, 80 ;CX used as element counter
CLD
REPNE SCAS ;Compare byte in string with byte in AL

## Slide 12
“String Manipulation Instructions”
REP / REPE / REPZ / REPNE / REPNZ (PREFIX)
(REPEAT STRING INSTRUCTION UNTIL SPECIFIED CONDITIONS EXIST)
REP is a prefix, which is written before one of the string instructions. It will cause the CX register to be decremented and the string instruction to be repeated until CX = 0.
For example, REP MOVSB, will continue to copy string bytes until the number of bytes loaded into CX has been copied.

## Slide 13
“String Manipulation Instructions”
REP / REPE / REPZ / REPNE / REPNZ (PREFIX)
(REPEAT STRING INSTRUCTION UNTIL SPECIFIED CONDITIONS EXIST)
REPE and REPZ are two mnemonics for the same prefix. They stand for repeat if equal and repeat if zero, respectively.
They are often used with the Compare String instruction or with the Scan String instruction.
They will cause the string instruction to be repeated as long as the compared bytes or words are equal (ZF = 1) and CX is not yet counted down to zero.
In other words, there are two conditions that will stop the repetition: CX = 0 or string bytes or words not equal.
REPE CMPSB ;Compare string bytes until end of string or until string bytes not equal

## Slide 14
“String Manipulation Instructions”
REP / REPE / REPZ / REPNE / REPNZ (PREFIX)
(REPEAT STRING INSTRUCTION UNTIL SPECIFIED CONDITIONS EXIST)
REPNE and REPNZ are also two mnemonics for the same prefix. They stand for repeat if not equal and repeat if not zero, respectively.
They are often used with the Compare String instruction or with the Scan String instruction.
They will cause the string instruction to be repeated as long as the compared bytes or words are not equal (ZF = 0) and CX is not yet counted down to zero.
REPNE SCASW ;Scan a string of word until a word in the string matches the word in AX or until all of the string has been scanned.