## Slide 1: “8086 Instruction Set” Lecture-20 M. M. Yasin myasin@ciitsahiwal.edu.pk

## Slide 2
“TRANSFER OF CONTROL INSTRUCTIONS”
JMP (UNCONDITIONAL JUMP TO SPECIFIED DESTINATION)
This instruction will fetch the next instruction from the location specified in the instruction.
If the destination is in the same code segment as the JMP instruction, then only the instruction pointer will be changed to get the destination location. This is referred to as a near jump.
If the destination for the jump instruction is in a segment with a name different from that of the segment containing the JMP instruction, then both the instruction pointer and the code segment register content will be changed to get the destination location. This referred to as a far jump.

## Slide 3
“TRANSFER OF CONTROL INSTRUCTIONS”
JA (JUMP IF ABOVE)
JNBE (JUMP IF NOT BELOW OR EQUAL)
If, after a compare or some other instructions which affect flags, the zero flag and the carry flag both are 0, this instruction will cause execution to jump to a label given in the instruction. If CF and ZF are not both 0, the instruction will have no effect on program execution.
CMP AX, 4371H ;Compare by subtracting 4371H from AX
JA NEXT ;Jump to label NEXT if AX above 4371H
CMP AX, 4371H ;Compare (AX – 4371H)
JNBE NEXT ;Jump to label NEXT if AX not below or equal to 4371H

## Slide 4
“TRANSFER OF CONTROL INSTRUCTIONS”
JNA (JUMP IF NOT ABOVE)
JBE (JUMP IF BELOW OR EQUAL)
If, after a compare or some other instructions which affect flags, either the zero flag or the carry flag is 1, this instruction will cause execution to jump to a label given in the instruction. If CF and ZF are both 0, the instruction will have no effect on program execution.
CMP AX, 4371H ;Compare (AX – 4371H)
JBE NEXT ;Jump to label NEXT if AX is below or equal to 4371H
CMP AX, 4371H ;Compare (AX – 4371H)
JNA NEXT ;Jump to label NEXT if AX not above 4371H

## Slide 5
“TRANSFER OF CONTROL INSTRUCTIONS”
JE (JUMP IF EQUAL)
JZ (JUMP IF ZERO)
This instruction is usually used after a Compare instruction. If the zero flag is set, then this instruction will cause a jump to the label given in the instruction.
CMP BX, DX ;Compare (BX-DX)
JE DONE ;Jump to DONE if BX = DX
IN AL, 8FH ;Read data from port 8FH
SUB AL, 30H ;Subtract the minimum value.
JZ START ;Jump to label START if the result of subtraction is 0

## Slide 6
“TRANSFER OF CONTROL INSTRUCTIONS”
JNE (JUMP NOT EQUAL)
JNZ (JUMP IF NOT ZERO)
This instruction is usually used after a Compare instruction. If the zero flag is 0, then this instruction will cause a jump to the label given in the instruction.
IN AL, F8H ;Read data value from port
CMP AL, 72 ;Compare (AL –72)
JNE NEXT ;Jump to label NEXT if AL ≠ 72
ADD AX, 0002H ;Add count factor 0002H to AX
DEC BX ;Decrement BX
JNZ NEXT ;Jump to label NEXT if BX ≠ 0

## Slide 7
“TRANSFER OF CONTROL INSTRUCTIONS”
JS (JUMP IF SIGNED / JUMP IF NEGATIVE)
This instruction will cause a jump to the specified destination address if the sign flag is set. Since a 1 in the sign flag indicates a negative signed number, you can think of this instruction as saying “jump if negative”.
ADD BL, DH ;Add signed byte in DH to signed byte in BL
JS NEXT ;Jump to label NEXT if result of addition is negative number

## Slide 8
“TRANSFER OF CONTROL INSTRUCTIONS”
JNS (JUMP IF NOT SIGNED / JUMP IF POSITIVE)
This instruction will cause a jump to the specified destination address if the sign flag is 0. Since a 0 in the sign flag indicate a positive signed number, you can think of this instruction as saying “jump if positive”.
DEC AL ;Decrement AL
JNS NEXT ;Jump to label NEXT if AL has not decremented to FFH

## Slide 9
“TRANSFER OF CONTROL INSTRUCTIONS”
JCXZ (JUMP IF THE CX REGISTER IS ZERO)
This instruction will cause a jump to the label given in the instruction, if the CX register contains all 0’s. The instruction does not look at the zero flag when it decides whether to jump or not.
JCXZ SKIP ;If CX = 0, skip the process
SUB [BX], 07H ;Subtract 7 from data value
SKIP: ADD C ;Next instruction

## Slide 10
“TRANSFER OF CONTROL INSTRUCTIONS”
LOOP (JUMP TO SPECIFIED LABEL IF CX ≠ 0 AFTER AUTO DECREMENT)
This instruction is used to repeat a series of instructions some number of times.
The number of times the instruction sequence is to be repeated is loaded into CX. Each time the LOOP instruction executes, CX is automatically decremented by 1.
If CX is not 0, execution will jump to a destination specified by a label in the instruction.
If CX = 0 after the auto decrement, execution will simply go on to the next instruction after LOOP.

## Slide 11
“TRANSFER OF CONTROL INSTRUCTIONS”
LOOP (JUMP TO SPECIFIED LABEL IF CX ≠ 0 AFTER AUTO DECREMENT)
MOV BX, OFFSET PRICES ;Point BX at first element in array
MOV CX, 40 ;Load CX with number of elements in array
NEXT: MOV AL, [BX] ;Get element from array
INC AL ;Increment the content of AL
MOV [BX], AL ;Put result back in array
INC BX; Increment BX to point to next location
LOOP NEXT ;Repeat until all elements adjusted

## Slide 12
“TRANSFER OF CONTROL INSTRUCTIONS”
CALL (CALL A PROCEDURE)
The CALL instruction is used to transfer execution to a subprogram or a procedure. There are two basic types of call near and far.
A near call is a call to a procedure, which is in the same code segment as the CALL instruction.
When the 8086 executes a near CALL instruction, it decrements the stack pointer by 2 and copies the offset of the next instruction after the CALL into the stack. This offset saved in the stack is referred to as the return address, because this is the address that execution will return to after the procedure is executed.
A near CALL instruction will also load the instruction pointer with the offset of the first instruction in the procedure.
A RET instruction at the end of the procedure will return execution to the offset saved on the stack which is copied back to IP.

## Slide 13
“TRANSFER OF CONTROL INSTRUCTIONS”
CALL (CALL A PROCEDURE)
A far call is a call to a procedure, which is in a different segment from the one that contains the CALL instruction. When the 8086 executes a far call, it decrements the stack pointer by 2 and copies the content of the CS register to the stack. It then decrements the stack pointer by 2 again and copies the offset of the instruction after the CALL instruction to the stack.
Finally, it loads CS with the segment base of the segment that contains the procedure, and loads IP with the offset of the first instruction of the procedure in that segment.
A RET instruction at the end of the procedure will return execution to the next instruction after the CALL by restoring the saved values of CS and IP from the stack.

## Slide 14
“TRANSFER OF CONTROL INSTRUCTIONS”
RET (RETURN EXECUTION FROM PROCEDURE TO CALLING PROGRAM)
The RET instruction will return execution from a procedure to the next instruction after the CALL instruction which was used to call the procedure.