## Slide 1: “8086 Instruction Set” Lecture-21 M. M. Yasin myasin@ciitsahiwal.edu.pk

## Slide 2
“Topics Covered”
Flag Manipulation Instructions (STC, CLC…)
Stack Related Instructions (PUSH, POP…)
Input-Output Instructions (IN, OUT…)

## Slide 3
“Flag Manipulation Instructions”
STC (Set Carry Flag)
This instruction sets the carry flag to 1.
CLC (Clear Carry Flag)
This instruction resets the carry flag to 0.
CMC (Complement Carry Flag)
This instruction complements the carry flag.

## Slide 4
“Flag Manipulation Instructions”
STI (Set Interrupt Flag)
Setting the interrupt flag to a 1 enables the INTR interrupt input of the 8086.
CLI (Clear Interrupt Flag)
This instruction resets the interrupt flag to 0.
If the interrupt flag is reset, the 8086 will not respond to an interrupt signal on its INTR input.

## Slide 5: Q. What would happen if a Non-Maskable interrupt occurs after a CLI instruction...??
When a Non-Maskable Interrupt (NMI) occurs after a CLI instruction, the NMI will still be processed immediately. The CLI instruction only disables maskable interrupts by clearing the interrupt flag (IF), but NMIs are designed to bypass this mechanism, ensuring they can be handled promptly even when the interrupt flag is cleared. This allows the system to respond to critical events without delay, maintaining system stability and reliability.

## Slide 6
“Stack Related Instructions”
PUSH – PUSH Source
The PUSH instruction decrements the stack pointer by 2 and copies a word from a specified source to the location in the stack segment to which the stack pointer points.
The source of the word can be general-purpose register, segment register, or memory.
The stack segment register and the stack pointer must be initialized before this instruction can be used.
PUSH BX ;Decrement SP by 2, copy BX to stack
PUSH DS ;Decrement SP by 2, copy DS to stack
PUSH BL ;Illegal, must push a word

## Slide 7
“Stack Related Instructions”
POP – POP Destination
The POP instruction copies a word from the stack location pointed to by the stack pointer to a destination specified in the instruction.
The destination can be a general-purpose register, a segment register or a memory location.
After the word is copied to the specified destination, the stack pointer is automatically incremented by 2 to point to the next word on the stack.
POP DX ;Copy a word from top of stack to DX, increment SP by 2
POP DS ;Copy a word from top of stack to DS, increment SP by 2

## Slide 8
“Stack Related Instructions”
PUSHF (PUSH FLAG REGISTER TO STACK)
The PUSHF instruction decrements the stack pointer by 2 and copies a word in the flag register to two memory locations in stack pointed to by the stack pointer.
POPF (POP WORD FROM TOP OF STACK TO FLAG REGISTER)
The POPF instruction copies a word from two memory locations at the top of the stack to the flag register and increments the stack pointer by 2.

## Slide 9
“Input-Output Instructions”
IN – IN Accumulator, Port
The IN instruction copies data from a port to the AL or AX register. If an 8-bit port is read, the data will go to AL. If a 16-bit port is read, the data will go to AX.
The IN instruction has two possible formats, (1) fixed port and (2) variable port.
For fixed port type, the 8-bit address of a port is specified directly in the instruction. With this form, any one of 256 possible ports can be addressed.
IN AL, OC8H ;Input a byte from port OC8H to AL
IN AX, 34H ;Input a word from port 34H to AX

## Slide 10
“Input-Output Instructions”
IN – IN Accumulator, Port
For the variable-port form of the IN instruction, the port address is loaded into the DX register before the IN instruction.
Since DX is a 16-bit register, the port address can be any number between 0000H and FFFFH. Therefore, up to 65,536 ports are addressable in this mode.
MOV DX, 0FF78H ;Initialize DX to point to port
IN AL, DX ;Input a byte from 8-bit port 0FF78H to AL
IN AX, DX ;Input a word from 16-bit port 0FF78H to AX

## Slide 11
“Input-Output Instructions”
IN – IN Accumulator, Port
The variable-port IN instruction has advantage that the port address can be computed or dynamically determined in the program.
For example, that an 8086-based computer needs to input data from 10 terminals, each having its own port address. Instead of having a separate procedure to input data from each port, you can write one generalized input procedure and simply pass the address of the desired port to the procedure in DX.

## Slide 12
“Input-Output Instructions”
OUT – OUT Port, Accumulator
The OUT instruction copies a byte from AL or a word from AX to the specified port. The OUT instruction has two possible forms, (1) fixed port and (2) variable port.
For the fixed port form, the 8-bit port address is specified directly in the instruction. With this form, any one of 256 possible ports can be addressed.
OUT 3BH, AL ;Copy the content of AL to port 3BH
OUT 2CH, AX ;Copy the content of AX to port 2CH

## Slide 13
“Input-Output Instructions”
OUT – OUT Port, Accumulator
For variable port form of the OUT instruction, the content of AL or AX will be copied to the port at an address contained in DX. Therefore, the DX register must be loaded with the desired port address before this form of the OUT instruction is used.
MOV DX, 0FFF8H ;Load desired port address in DX
OUT DX, AL ;Copy content of AL to port FFF8H
OUT DX, AX ;Copy content of AX to port FFF8H