## Slide 1: “Internal Memory” in [ Computer Organization and Assembly Language ] Lecture-24 M. M. Yasin myasin@ciitsahiwal.edu.pk

## Slide 2
“Topics Covered”
Section 5.1 (Semiconductor Main Memory)
  Organization
  Types of ROM
  DRAM and SRAM
Section 5.3 (Advanced DRAM Organization)
  Synchronous DRAM
  Rambus DRAM
  Cache DRAM

## Slide 3
“Computer Memory System”
Computer memory is organized into a hierarchy:
At the highest level (closest to the processor), are the processor Registers.
Next comes one or more levels of Cache. When multiple levels are used, they are denoted L1, L2, and so on.
Next comes Main Memory, which is usually made out of dynamic random-access memory (DRAM).
All of these are considered internal to the computer system.
The hierarchy continues with external memory, with the next level typically being a fixed Hard Disk,
and one or more levels below that consisting of removable media such as Optical Disks and Tape.

## Slide 4
“Types of Read-only Memory (ROM)”
1. Read-Only Memory (ROM):
It contains data that cannot be changed once programmed.
These are Non-volatile.
A ROM is created like any other integrated chip (IC), with the data actually wired into the chip as part of the fabrication process.
Other available ROMs are:
2. Programmable ROM (PROM):
Writing process is performed electrically, and it is not a part of the fabrication process. i.e., can be done later (after fabrication).

## Slide 5
“Types of Read-only Memory (ROM)”
3. Optically erasable programmable read-only memory (EPROM):
They can be read or written electrically.
However before a write operation , all of the storage cells must be erased to the same initial state by exposure of the packaged chip to ultraviolet radiation.
Note: Therefore, EPROMs can be altered multiple times, whereas ROM and PROM don’t.

## Slide 6
“Types of Read-only Memory (ROM)”
4. Electrically erasable programmable read-only memory (EEPROM):
They can be written at any time without erasing prior contents.
Non-Volatile.
Data updatable in place, using ordinary bus control, address and data lines.
More expensive than EPROM.
Less dense. i.e., fewer bits per chip.

## Slide 7
“Types of Read-only Memory (ROM)”
5. Flash Memory:
Named as “Flash” because of the speed with which it can be reprogrammed.
Intermediate b/w EPROM and EEPROM in both cost and functionality.
Like EPROM, flash memory uses only one transistor per bit, more dense than EEPROM.
Like EEPROM, flash memory uses an electrical erasing technology.
  Entire flash memory can be erased in few seconds.
  A block of memory can be erased instead of entire chip.
  However flash memory doesn’t provide byte level erasure.

## Slide 8
“Random Access Memory - Characteristics”
1. Reading from the memory and Writing into the memory is easy and fast.
2. RAM is volatile. i.e., needs constant power supply.
“Random Access Memory - Technologies”
1. Dynamic RAM.
2. Static RAM.

## Slide 9
“Random Access Memory - Technologies”
1. DRAM: made with cells that store data as charge on capacitors.
Capacitors have natural tendency to discharge, therefore require periodic refreshing to maintain data storage.
The term Dynamic refers to this tendency of the stored charge leakage, even with power continuously applied.
One cell consists of one transistor and a capacitor to store 1 bit.
Transistor acts as a switch, and
Presence of charge on the capacitor shows binary 1 , and
Absence of charge represents binary 0.
Address line is used to open/close the transistor (switch), and
Bit line is used to read/write data(1 bit) from/to the capacitor.

## Slide 10
“Random Access Memory - Technologies”
2. SRAM: Traditional flip-flop logic gates are used to store binary 1 and 0 values.
No refresh is needed to retain data.
One cell consists of 2+4 transistors.
2 Transistors acts as a switch.
4 Transistors (cross-connected) produces a logic state (0 or 1), and
Address line is used to open/close the 2 transistors (switch), and
Bit line is used to read/write data(1 bit) from/to the 4 transistors.

## Slide 11
“DRAM versus SRAM”
Both are volatile.
DRAM is simple and less expensive.
DRAM is more dense. i.e., more cells/unit area.
DRAMs tend to be favored for large memory requirements.
SRAMs are faster than DRAMs.
Because of these relative characteristics,
SRAM is used for cache memory (both on and off chip), and
DRAM is used for main memory.

## Slide 12
“Advanced DRAM Organization”
Processor and Internal Memory interface is the most important in the entire computer system.
DRAM is the basic building block of main memory remains the DRAM chip, which is low in performance.
In order to solve this performance mismatch, one or more levels of high-speed SRAM cache (L1, L2, L3) between the DRAM Main Memory and the Processor has been inserted.
But SRAM is expensive than DRAM, and expanding cache size beyond a certain point doesn’t produce fruitful results.

## Slide 13
“Advanced DRAM Organization”
A number of enhancements to the basic DRAM architecture are: SDRAM, DDR-DRAM, RDRAM and CDRAM schemes.
Synchronous DRAM (S-DRAM)
One of the most widely used forms of DRAM is the synchronous DRAM (SDRAM).
Unlike the traditional DRAM, which is asynchronous, the SDRAM exchanges data with the processor synchronized to an external clock signal and running at the full speed of the processor/memory bus without imposing wait states.
The SDRAM performs best when it is transferring large blocks of data serially, such as for applications like word processing, spreadsheets, and multimedia.

## Slide 14
“Advanced DRAM Organization”
Rambus DRAM (R-DRAM)
RDRAM, developed by Rambus, has been adopted by Intel for its Pentium and Itanium processors.
It has become the main competitor to SDRAM.
RDRAM chips are vertical packages, with all pins on one side.
The chip exchanges data with the processor over 28 wires no more than 12cm long.
The bus can address up to 320 RDRAM chips and is rated at 1.6 GBps.

## Slide 15
“Advanced DRAM Organization”
Double Data Rate SDRAM (DDR-SDRAM)
SDRAM is limited by the fact that it can only send data to the processor once per bus clock cycle. This version of SDRAM, referred to as DDR-SDRAM can send data twice per clock cycle, once on the rising edge of the clock pulse and once on the falling edge.
DDR DRAM was developed by the JEDEC Solid State Technology Association. Numerous companies make DDR chips, which are widely used in desktop computers and servers.

## Slide 16
“Advanced DRAM Organization”
Double Data Rate DRAM (DDR-DRAM)
There have been two generations of improvement to the DDR technology: DDR2, DDR3.
DDR2 increases the data transfer rate by:
(a) Increasing the operational frequency of the RAM chip.
(b) Increasing the prefetch buffer from 2 bits to 4 bits per chip.
Note: The prefetch buffer is a memory cache located on the RAM chip. The buffer enables the RAM chip to preposition bits to be placed on the data base as rapidly as possible.

## Slide 17
“Advanced DRAM Organization”
Double Data Rate DRAM (DDR-DRAM)
There have been two generations of improvement to the DDR technology: DDR2 and DDR3.
DDR3, introduced in 2007, increases the prefetch buffer size to 8 bits.
Theoretically,
 A DDR module can transfer data at a clock rate from 200 to 600 MHz.
 A DDR2 module transfers at a clock rate of 400 to 1066 MHz.
A DDR3 module transfers at a clock rate of 800 to 1600 MHz.
In practice, somewhat smaller rates are achieved.

## Slide 18
“Advanced DRAM Organization”
Cache DRAM (C-DRAM)
Cache DRAM (CDRAM), developed by Mitsubishi, integrates a small SRAM cache (16 Kb) onto a generic DRAM chip.
The SRAM on the CDRAM can be used in two ways:
First, it can be used as a true cache, consisting of a number of 64-bit lines. The cache mode of the CDRAM is effective for ordinary random access to memory.
The SRAM on the CDRAM can also be used as a buffer to support the serial access of a block of data. For example, to refresh a bit-mapped screen, the CDRAM can prefetch the data from the DRAM into the SRAM buffer. Subsequent accesses to the chip result in accesses solely to the SRAM.